Report
by Mike Karamousadakis

1) Goal and Specifications

The goal of my 2 month Internship in 01Mechatronics was to build a 6dof robot manipulator, using Python for programming and the Servo Motors provided by the company. The specifications were, the robot to have as much smoothness in it’s motion as possible, taking into account the specific Servo Motors.

2) Structure

The structure of the work is summarized in the following diagram:

Description of the Robot
6dof_description.urdf

Robot Testing Script
6dof_commander.py
Inverse Kinematics Module
ikpy module
Layer of SMS commands
sms_library_oo.py

API for the Robotic Chain;
inside functions like
move_xyz_abc or move_circ
robotic_chain.py
Transformations required for the Robot
Implemented inside geometry_utils.py

3.1. Layer of SMS commands
The SuperModified™ combo of miniature PCBs is an all-in one motor control solution. Incorporating a 15-bit magnetic absolute encoder, an 8-bit, 20MHz AVR ATMega328p microcontroller and a 5-Amp MosFet H-bridge at an astonishing outline of 16mm x 16mm x 13.2 mm it is ideal for space constrained applications. The overall dimensions allow for this motion control system to be installed inside a standard RC servo, transforming the device to a full functionality servo motor. The 01TMSuperModified is a highly cost effective solution, delivering closed loop PID control at 9.765 KHz, with advanced motion profiling capabilities and many other features. The process for building the robot could not be initiated without a proper API for controlling the robot’s motors. As we wanted the robot API to be implemented in Python, we implemented the SMS API also in Python. The manual for this API is in [1] but we quote some lines here as a reference:
The 01TMPython Library contains all the functions needed to interface to the
Supermodified controller. Each function is actually an implementation of a command of the 01
TM
protocol. The command set of the Supermodified controller
is presented in detail in section 11 of the Supermodified datasheet.
There are generally 3 types of commands.
Set commands
All set commands are implemented as Python functions that accept 1 or more
inputs and return one output.
The first (or only) input is always the motor ID on the bus. The motor ID can only
be changed by using the SuperModified Commander (01
TM
stand-alone
application) and must be unique for every controller on the bus. All Supermodified
controllers are shipped with a default motor ID=4.
If the command does not transmit any additional information to the Supermodified
controller then the function has only one input and only one output. The input is
the motor ID and the output is whether the call was successful or not.
eg.
def start(mid):
...
return not getResponse()[0]
The above is the start command and starts the control to the motor. It must be
executed before any command that attempts to move the motor.
If the command has one or more data arguments that must be passed to the
controller then the Python function is like below:
eg.
def moveWithVelocity(mid, val):
...
return not getResponse()[0]
where mid is motor Id. val is velocity Ticks per second.
The above is the Move With Velocity Command that tells the motor to move at
val
velocity. Note that the
mid
input is always first.
Or another example:
01
TM
SuperModified
4/5
def setDigitalOutputs(mid, dio1, dio2, dio3):
...
return not getResponse()[0]
The above command sets or resets the controller’s digital outputs according to
inputs
dio1,dio2,dio3
and according to Digital IO configuration.
Note:
The set command Functions return not
getResponse()[0]
for a reason
explained in the comments of the code.
Get commands
All get commands are implemented as Python functions that accept 1 input and
return 1 or more outputs.
The input is always the Motor ID and the first output is always the success or
failure of the command. The rest of the outputs depend on the command.
For example:
def getPosition(mid):
...
return getResponse()
This Python function can be used to read the position of the motor in encoder ticks
(32768 ticks per revolution). The position will be stored in
getPosition(mid)[1]
.
The
success of the command will be in
getPosition(mid)[0].
The motor that is
communicated is the one with
mid.
Accordingly commands that have more outputs,
eg.
def getDigitalIOConfiguration(mid, dio):
...
return getDigitalIOResponse()
This Python function can be used to read the digital IO configuration. The
bits
dio1, dio2, dio3 are stored in getDigitalIOConfiguration
(mid, dio)
[1-3] respectively
.
The success of the command will be in
getDigitalIOConfiguration
(mid,
dio)
[0]
.
The motor that is communicated is the one with
mid.
Broadcast commands
All broadcast commands are implemented as Python function with only one output
which is always True.
eg.
def broadcastStart():
...
return True
The above command starts all motors on the bus.

3.2 Creation of the URDF file

URDF is an XML format for representing a robot model. The creation of the urdf file followed the online tutorial in [2]. The main idea here, is that the robot consists of two parts: links and joints.

The joints are the key players in the process of creating a urdf file. Every joint has a parent link and a child link, an origin and an axis. These two variables are filled with the following procedure: Starting from the base, we compute the distance and the rotation with respect to the previous coordinate system of every joint and we fill in the values to the <origin> node (namely to xyz and rpy). In the <axis> tag we fill in the transformation between the local axis and the axis of the current joint rotation (if we fill it having in mind the DH parameters, this will be always “0 0 1” because in the DH convention, the joint rotates always around the local z-axis).

The links are elements which describe how the joints are connected. They have visual and collision elements which represent their visual characteristics and their collision parameters respectively.

3.3 Forward, Inverse and Differential Kinematics
Having a system of rigid bodies, especially a robotic chain, we need a way to describe the location of a point in 3D space expressed in the coordinate system of the end effector, expressed in the global coordinate system which almost always is the coordinate system of the robot base. For that, computation of the transformation matrices from the global coordinate system (robot base) to the end-effector coordinate system is needed.

Therefore, the geometric modeling needed, is computed with the DH method. This method in practice, places the intermediate coordinate systems with a systematic way under the following rules:
- The direction of the z axis of the frame i-1 , matches the direction of movement of joint i .
- The direction of the x_i axis is along the common perpendicular of z_i and z_{ i-1 } , or if the axes intersect, normal to the plane containing the two axes.
- The transition from previous coordinate system to the next, is carried out with the following successive rotations and translations:
1. Rotate the frame i-1 around z_{ i-1 } by θ_i
2. Translate the frame i-1 along z_{ i-1 } axis by d_i
3. Translate the frame i-1 along x_{ i-1 } axis(which is now aligned with x_{ i } ) by a_i
4. Rotate the frame i-1 around the x_{ i-1 } axis by α_i
With the following rules, for the description of the geometric model a matrix with the DH parameters mentioned above is enough.
From the description of the model, the Transition Matrix from the i-1 to i frame is computed, based on the Matrix with the DH parameters:

……

For the specific robotic manipulator, the coordinate systems obeying the DH convention and the DH parameters of the model are presented below:

….

Photo in Rviz

Forward Kinematics

By the time the individual matrices have been computed with the DH parameters, the solution of the forward kinematics problem, i.e the determination of the position and the orientation of the end-effector, given the relative position of the joints, is nothing more than a combination of the individual transformations, i.e the multiplication of the matrices A_i^{ i-1 },i=1,2,3,4,5,6 ( 6 equiv E) . So the solution of the forward kinematics problem is the following:
T = A_1^0 *A^1_2*A^2_3*A^3_4*A^4_5*A^5_{ 6 equiv E}

3.6 Integration of the Inverse Kinematics Module

To shorten the work we had to do, we searched and found the Inverse Kinematics Module (aka ikpy) developed by Pierre Manceron. It uses numerical analysis algorithms to solve the inverse kinematics problem, i.e. given the position and orientation of the end-effector in 3D Space, find the positions of the individual joints. Of course the solution is not unique, so an optimization algorithm (specifically Levenberg–Marquardt algorithm or LMA) is also used. This module was highly utilized and complemented for the needs of the particular project. Specifically there were added some functions which implemented all the transformations between the representation with Euler angles, representation with quaternions and angle-axis representation. Secondly there were some modifications of the module, to support the computation and use of the Jacobian Matrix of the robot.

3.4 Trajectory Generation with Polynomial Interpolation

  For the design of the trajectory, polynomial interpolation was used. Specifically, a trajectory of three phases was created (Acceleration – Steady Speed – Deceleration), demanding continuity in acceleration, with interpolation polynomials of 4th degree in acceleration and deceleration, and polynomial of 1st degree in the phase of steady speed. The above procedure was utilized not only for the circular and line trajectory but also for the angle trajectory (using angle-axis representation). A helpful figure follows:

Line Trajectory

For the line trajectory, the three-phase interpolation was used for one variable and the trajectories of the other two variables were created from the parametric equations of the line:

{x-x_start} over a = {y-y_start} over b = {z-z_start} over c , where a, b, c are respectively:
a = x_start - x_final newline b = y_start - y_final newline c = z_start - z_final

Circular Trajectory

In order to determine which circular trajectory, in 3D space, the robot would follow between the starting point and the goal point, another point (the middle point) should be determined, because three points determine one and only circle (Geometry Theorem). So the algorithm (described also in [4]) is as follows:
1. Compute the cross product of two vectors formed from the three points, which is also a vector. The result is a vector perpendicular to the plane of the three points.
2. Find the parameters a,b,c,d of the plane, which is in the form ax+by+cz+d = 0 ( 1 ) , using the perpendicular vector and another point.
3. To find the center of the circle and the radius, solve for the crossing of a sphere and the above plane (1). Solve for a variable in (1) and use the formula in (2):
  left lbrace binom{( x_start-x_center )^2 + ( y_start-y_center )^2 + ( z_start-z_center )^2= R^2}{( x_final-x_center )^2 + ( y_final-y_center )^2 + ( z_final-z_center )^2= R^2} right rbrace ( 2 )
  After finding the two coordinates from (2), use (1) to find the other coordinate of the point in the center of the circle.
4. Specify a new coordinate system (u,v,w) with w being the perpendicular vector found in 1. Use the three-phase interpolation for a variable θ , which will span the arc of the circle, from the starting point ( θ = 0) to the final point. For θ to be zero at the starting point, specify the vector u to be aligned with the vector u_{ Start,Origin } , which is the vector starting from the origin to the starting point. After a time law for θ has been specified, plug in the values of θ to the known equations of the circle to find the u and v coordinates of the point in the circle, then apply the rotation matrix R_{O}^{u,v,w} = [ u,v,w ] to transform the u, v coordinates to, for example, x and y coordinates and add the vector u_{ center,origin } to find the x and y coordinates of the point with respect to the origin. Finally, find the z coordinate of the point by substitution in (1).

Angle Trajectory

The implemented angle trajectory is described very nicely in [5] and it is strongly recommended to examine the relative chapter. The basic concept is that for every rotation there is an angle and an axis around which the rotation with the angle moves the starting pose to the final pose. The axis is a fixed vector, so very easy to compute and for the angle, a time law can be created by using again the three-phase polynomial interpolation. Again, please refer to [5] in the section of angle axis in the chapter of trajectory generation.

3.5 Actual Inverse (Differential) Kinematics Implementation

The actual implementation of the motion control loop started with the use of the inverse jacobian algorithm for inverse kinematics although abandoned soon for the sake of more stability and robustness. Seeking more robustness led to utilize the damped least squares (dls) algorithm described in [3], which proved highly more robust and with a little tunning it didn’t lose the ability to track the desired trajectory provided. As far as the orientation trajectory is concerned, quaternions were used as a more robust option from euler angles and angle axis representation. The basic steps of the algorithm are the following: